## Slide 1: Lecture 12: Manycore GPU Architectures and Programming, Part 2
CSCE 790: Parallel Programming Models for Multicore and Manycore Processors
Department of Computer Science and Engineering
Yonghong Yan
yanyh@cse.sc.edu
http://cse.sc.edu/~yanyh

## Slide 2: How is the GPU controlled?
The CUDA API is split into:
  The CUDA Management API
  The CUDA Kernel API
The CUDA Management API is for a variety of operations
  GPU memory allocation, data transfer, execution, resource creation
  Mostly regular C function and calls
The CUDA Kernel API is used to define the computation to be performed by the GPU
  C extensions

## Slide 3: How is the GPU controlled?
A CUDA kernel:
  Defines the operations to be performed by a single thread on the GPU
  Just as a C/C++ function defines work to be done on the CPU
  Syntactically, a kernel looks like C/C++ with some extensions
        __global__ void kernel(...) {
        ...
        }
  Every CUDA thread executes the same kernel logic (SIMT)
  Initially, the only difference between threads are their thread coordinates

## Slide 4: How are GPU threads organized?
CUDA thread hierarchy
  Warp = SIMT Group
  Thread Block = SIMT Groups that run concurrently on an SM
  Grid = All Thread Blocks created by the same kernel launch
Launching a kernel is simple and similar to a function call.
  kernel name and arguments
  # of thread blocks/grid and # of threads/block to create:
  kernel<<<nblocks,
  threads_per_block>>>(arg1, arg2, ...);

## Slide 5: How are GPU threads organized?
In CUDA, only thread blocks and grids are first-class citizens of the programming model.
The number of warps created and their organization are implicitly controlled by the kernel launch configuration, but never set explicitly.
  kernel<<<nblocks, threads_per_block>>>(arg1, arg2, ...);
kernel launch configuration

## Slide 6: How are GPU threads organized?
GPU threads can be configured in one-, two-, or three-dimensional layouts
  One-dimensional blocks and grids:
    int nblocks = 4;
    int threads_per_block = 8;
    kernel<<<nblocks, threads_per_block>>>(...);
Block 0
Block 1
Block 2
Block 3

## Slide 7: How are GPU threads organized?
GPU threads can be configured in one-, two-, or three-dimensional layouts
  Two-dimensional blocks and grids:
    dim3 nblocks(2,2)
    dim3 threads_per_block(4,2);
    kernel<<<nblocks, threads_per_block>>>(...);

## Slide 8: How are GPU threads organized?
GPU threads can be configured in one-, two-, or three-dimensional layouts
  Two-dimensional grid and one-dimensional blocks:
    dim3 nblocks(2,2);
    int threads_per_block = 8;
    kernel<<<nblocks, threads_per_block>>>(...);

## Slide 9: How are GPU threads organized?
On the GPU, the number of blocks and threads per block is exposed through intrinsic thread coordinate variables:
  Dimensions
  IDs
Variable | Meaning
gridDim.x, gridDim.y, gridDim.z | Number of blocks in a kernel launch.
blockIdx.x, blockIdx.y, blockIdx.z | Unique ID of the block that contains the current thread.
blockDim.x, blockDim.y, blockDim.z | Number of threads in each block.
threadIdx.x, threadIdx.y, threadIdx.z | Unique ID of the current thread within its block.

## Slide 10: How are GPU threads organized?
to calculate a globally unique ID for a thread on the GPU inside a one-dimensional grid and one-dimensional block:
    kernel<<<4, 8>>>(...);
__global__ void kernel(...) {
int tid = blockIdx.x * blockDim.x + threadIdx.x;
...
}
Block 0
Block 1
Block 2
Block 3
blockIdx.x = 2;
blockDim.x = 8;
threadIdx.x = 2;
0 1 2 3 4 5 6 7
8

## Slide 11: How are GPU threads organized?
Thread coordinates offer a way to differentiate threads and identify thread-specific input data or code paths.
  Link data and computation, a mapping
__global__ void kernel(int *arr) {
int tid = blockIdx.x * blockDim.x + threadIdx.x;
if (tid < 32) {
arr[tid] = f(arr[tid]);
} else {
arr[tid] = g(arr[tid]);
}
code path for threads with tid < 32
code path for threads with tid >= 32
Thread Divergence: recall that useless code path is executed, but then disabled in SIMT execution model

## Slide 12: How is GPU memory managed?
CUDA Memory Management API
  Allocation of GPU memory
  Transfer of data from the host to GPU memory
  Free-ing GPU memory
  Foo(int A[][N]) { }
Host Function | CUDA Analogue
malloc | cudaMalloc
memcpy | cudaMemcpy
free | cudaFree

## Slide 13: How is GPU memory managed?
cudaError_t cudaMalloc(void **devPtr, size_t size);
  Allocate size bytes of GPU memory and store their address at *devPtr
cudaError_t cudaFree(void *devPtr);
  Release the device memory allocation stored at devPtr
  Must be an allocation that was created using cudaMalloc

## Slide 14: How is GPU memory managed?
cudaError_t cudaMemcpy(
void *dst, const void *src, size_t count,
enum cudaMemcpyKind kind);
  Transfers count bytes from the memory pointed to by src to dst
  kind can be:
    cudaMemcpyHostToHost,
    cudaMemcpyHostToDevice,
    cudaMemcpyDeviceToHost,
    cudaMemcpyDeviceToDevice
  The locations of dst and src must match kind, e.g. if kind is cudaMemcpyHostToDevice then src must be a host array and dst must be a device array

## Slide 15: How is GPU memory managed?
void *d_arr, *h_arr;
h_addr = … ; /* init host memory and data */
// Allocate memory on GPU and its address is in d_arr
cudaMalloc((void **)&d_arr, nbytes);
// Transfer data from host to device
cudaMemcpy(d_arr, h_arr, nbytes,
cudaMemcpyHostToDevice);
// Transfer data from a device to a host
cudaMemcpy(h_arr, d_arr, nbytes,
cudaMemcpyDeviceToHost);
// Free the allocated memory
cudaFree(d_arr);

## Slide 16: CUDA Program Flow
At its most basic, the flow of a CUDA program is as follows:
  Allocate GPU memory
  Populate GPU memory with inputs from the host
  Execute a GPU kernel on those inputs
  Transfer outputs from the GPU back to the host
  Free GPU memory
Let’s take a look at a simple example that manipulates data

## Slide 17: AXPY Example with OpenMP: Multicore
y = α·x + y
  x and y are vectors of size n
  α is scalar
Data (x, y and a) are shared
  Parallelization is relatively easy

## Slide 18: CUDA Program Flow
AXPY is an embarrassingly parallel problem
  How can vector addition be parallelized?
  How can we map this to GPUs?
Each thread does one element
A
B
C

## Slide 19: AXPY Offloading To a GPU using CUDA
Memory allocation on device
Memcpy from host to device
Launch parallel execution
Memcpy from device to host
Deallocation of dev memory

## Slide 20: CUDA Program Flow
Consider the workflow of the example vector addition vecAdd.cu:
  Allocate space for A, B, and C on the GPU
  Transfer the initial contents of A and B to the GPU
  Execute a kernel in which each thread sums Ai and Bi, and stores the result in Ci
  Transfer the final contents of C back to the host
  Free A, B, and C on the GPU
Modify to C = A+B+C
A = B*C;
we will need both C and A in the host side after GPU computation.
Compile and running
  Use codd from gpu_code_examples folder
  $nvcc –Xcompiler –fopenmp vectorAdd.cu
  $./a.out
Notes: By analyzing the input and out data for each kernel, we know which array should be copied in and which one should be copied out before and after the kernel execution.

## Slide 21: More Examples and Exercises
Matvec:
  Version 1: each thread computes one element of the final vector
  Version 2:
Matmul:
  Version 1: each thread computes one row of the final matrix C

## Slide 22: CUDA SDK Examples
CUDA Programming Manual:
  http://docs.nvidia.com/cuda/cuda-c-programming-guide
CUDA SDK Examples on CUDA installation folder
  E.g. /usr/local/cuda-8.0/samples/
Copy to your home folder
  cp –r /usr/local/cuda-8.0/samples ~/CUDA_samples
Do a “make” in the folder, and it will build all the sources
Or go to a specific example folder and make, it will build only the binary
Find ones you are interested in and run to see

## Slide 23: Inspecting CUDA Programs
Debugging CUDA program:
  cuda-gdb debugging tool, like gdb
Profiling a program to examine the performance
  Nvprof tool, like gprof
  Nvprof ./vecAdd
Notes: For instructor: example walkthrough of cuda-gdb applied to sumArraysOnGPU-small-case.cu

## Slide 24: Manycore GPU Architectures and Programming: Outline
Introduction
  GPU architectures, GPGPUs, and CUDA
GPU Execution model
CUDA Programming model
Working with Memory in CUDA
  Global memory, shared and constant memory
Streams and concurrency
CUDA instruction intrinsic and library
Performance, profiling, debugging, and error handling
Directive-based high-level programming model
  OpenACC and OpenMP
Notes: GPUs have developed from graphics cards into a platform for high performance computing and perhaps the most important development in HPC for many years.

## Slide 25: Storing Data on the GPU
A memory hierarchy emulates a large amount of low-latency memory
  Cache data from a large, high-latency memory bank in a small low-latency memory bank
DRAM
L2 Cache
L1 Cache
CPU Memory Hierarchy

## Slide 26: Storing Data on the GPU
SIMT Thread Groups on a GPU
SIMT Thread Groups on an SM
SIMT Thread Group
Registers
Local Memory
On-Chip Shared Memory
Global Memory
Constant Memory
Texture Memory
The CUDA Memory Hierarchy is more complex than the CPU memory hierarchy
  Many different types of memory, each with special-purpose characteristics
  More explicit control over data movement

## Slide 27: Storing Data on the GPU
Registers
  Lowest latency memory space on the GPU
  Private to each CUDA thread
  Constant pool of registers per-SM divided among threads in resident thread blocks
  Architecture-dependent limit on number of registers per thread
  Registers are not explicitly used by the programmer, implicitly allocated by the compiler
  -maxrregcount compiler option allows you to limit # registers per thread

## Slide 28: Storing Data on the GPU
L1 Cache
L2 Cache
Global Memory
GPU Caches
  Behaviour of GPU caches is architecture-dependent
  Per-SM L1 cache stored on-chip
  Per-GPU L2 cache stored off-chip, caches values for all SMs
  Due to parallelism of accesses, GPU caches do not follow the same LRU rules as CPU caches

## Slide 29: Storing Data on the GPU
Shared Memory
Transfer
Shared Memory
  Declared with the __shared__ keyword
  Low-latency, high bandwidth
  Shared by all threads in a thread block
  Explicitly allocated and managed by the programmer, manual L1 cache
  Stored on-SM, same physical memory as the GPU L1 cache
  On-SM memory is statically partitioned between L1 cache and shared memory

## Slide 30: Storing Data on the GPU
Constant Memory
Constant Cache
Constant Memory
  Declared with the __constant__ keyword
  Read-only
  Limited in size: 64KB
  Stored in device memory (same physical location as Global Memory)
  Cached in a per-SM constant cache
  Optimized for all threads in a warp accessing the same memory cell

## Slide 31: Storing Data on the GPU
Texture Memory Read-Only Cache
Texture Memory
Texture Memory
  Read-only
  Stored in device memory (same physical location as Global Memory)
  Cached in a texture-only on-SM cache
  Optimized for 2D spatial locality (caches commonly only optimized for 1D locality)
  Explicitly used by the programmer
  Special-purpose memory

## Slide 32: Storing Data on the GPU
L1 Cache
L2 Cache
Global Memory
Global Memory
  Large, high-latency memory
  Stored in device memory (along with constant and texture memory)
  Can be declared statically with __device__
  Can be allocated dynamically with cudaMalloc
  Explicitly managed by the programmer
  Optimized for all threads in a warp accessing neighbouring memory cells

## Slide 33: Storing Data on the GPU

## Slide 34: Storing Data on the GPU

## Slide 35: Concentrate On:
Global memory
Shared memory
Constant memory

## Slide 36: Static Global Memory
Static Global Memory has a fixed size throughout execution time:
__device__ float devData;
__global__ void checkGlobalVariable()
printf(“devData has value %f\n”, devData);
}
Initialized using cudaMemcpyToSymbol:
cudaMemcpyToSymbol(devData, &hostData,sizeof(float));
Fetched using cudaMemcpyFromSymbol:
cudaMemcpyFromSymbol(&hostData, devData, sizeof(float));
Notes: Instructor note: you can choose to use globalVariable.cu from Chapter 4 here as an illustrative example. In general, static global memory has limited usefulness so don’t feel the need to spend a large amount of time on the topic.

## Slide 37: Dynamic Global Memory
We have already seen dynamic global memory
  cudaMalloc dynamically allocates global memory
  cudaMemcpy transfers to/from global memory
  cudaFree frees global memory allocated by cudaMalloc
cudaMemcpy supports 4 types of transfer:
  cudaMemcpyHostToHost, cudaMemcpyHostToDevice, cudaMemcpyDeviceToHost, cudaMemcpyDeviceToDevice
You can also memset global memory
  cudaError_t cudaMemset(void *devPtr, int value, size_t count);
Notes: Instructor note: use the memTransfer.cu example from Chapter 4 to illustrate dynamic global memory allocation, transfer, freeing.

## Slide 38: Global Memory Access Patterns
CPU caches are optimized for linear, iterative memory accesses
  Cache lines ensure that accessing one memory cell brings neighbouring memory cells into cache
  If an application exhibits good spatial or temporal locality (which many do), later references will also hit in cache
CPU
System Memory
Cache

## Slide 39: Global Memory Access Patterns
GPU caching is a more challenging problem
  Thousands of threads cooperating on a problem
  Difficult to predict the next round of accesses for all threads
For efficient global memory access, GPUs instead rely on:
  Large device memory bandwidth
  Aligned and coalesced memory access patterns
  Maintaining sufficient pending I/O operations to keep the memory bus saturated and hide global memory latency

## Slide 40: Global Memory Access Patterns
Achieving aligned and coalesced global memory accesses is key to optimizing an application’s use of global memory bandwidth
  Coalesced: the threads within a warp reference memory addresses that can all be serviced by a single global memory transaction (think of a memory transaction as the process of bring a cache line into the cache)
  Aligned: the global memory accesses by threads within a warp start at an address boundary that is an even multiple of the size of a global memory transaction

## Slide 41: Global Memory Access Patterns
A global memory transaction is either 32 or 128 bytes
  The size of a memory transaction depends on which caches it passes through
  If L1 + L2: 128 byte
  If L2 only: 32 bytes
  Which caches a global memory transaction passes through depends on GPU architecture and the type of access (read vs. write)

## Slide 42: Global Memory Access Patterns
When is a global memory read cached in L1?
If the L1 cache is not used for global memory reads, the L2 cache is always used
Compute Capability | Reads Cacheable in L1? | Cached by Default?
Fermi (2.x) | Yes | Yes
Kepler (3.x) | No | No
Kepler K40 and later (3.5 and up) | Yes | No

## Slide 43: Global Memory Access Patterns
When is a global memory write cached in L1? Never
Global memory writes are cached in the L2 cache
Compute Capability | Reads Cacheable in L1? | Cached by Default?
Fermi (2.x) | No | No
Kepler (3.x) | No | No
Kepler K40 and later (3.5 and up) | No | No

## Slide 44: Global Memory Access Patterns
Aligned and Coalesced Memory Access (w/ L1 cache)
With 128-byte access, a single transaction is required and all of the loaded bytes are used

## Slide 45: Global Memory Access Patterns
Misaligned and Coalesced Memory Access (w/ L1 cache)
With 128-byte access, two memory transactions are required to load all requested bytes. Only half of the loaded bytes are used.

## Slide 46: Global Memory Access Patterns
Misaligned and Uncoalesced Memory Access (w/ L1 cache)
With uncoalesced loads, many more bytes loaded than requested

## Slide 47: Global Memory Access Patterns
Misaligned and Uncoalesced Memory Access (w/ L1 cache)
One factor to consider with uncoalesced loads: while the efficiency of this access is very low it may bring many cache lines into L1/L2 cache which are used by later memory accesses. The GPU is flexible enough to perform well, even for applications that present suboptimal access patterns.

## Slide 48: Global Memory Access Patterns
Memory accesses that are not cached in L1 cache are serviced by 32-byte transactions
  This can improve memory bandwidth utilization
  However, the L2 cache is device-wide, higher latency than L1, and still relatively small  many applications may take a performance hit if L1 cache is not used for reads

## Slide 49: Global Memory Access Patterns
Aligned and Coalesced Memory Access (w/o L1 cache)
With 32-byte transactions, four transactions are required and all of the loaded bytes are used

## Slide 50: Global Memory Access Patterns
Misaligned and Coalesced Memory Access (w/o L1 cache)
With 32-byte transactions, extra memory transactions are still required to load all requested bytes but the number of wasted bytes is likely reduced, compared to 128-byte transactions.

## Slide 51: Global Memory Access Patterns
Misaligned and Uncoalesced Memory Access (w/o L1 cache)
With uncoalesced loads, more bytes loaded than requested but better efficiency than with 128-byte transactions
Notes: Instructor Note: At this point, walk through the readSegment.cu example on pgs 165-168 in the book to demonstrate the actual performance implications of misaligned reads using nvprof.

## Slide 52: Global Memory Access Patterns
Global Memory Writes are always serviced by 32-byte transactions
Notes: Instructor Note: At this point, walk through the writeSegment.cu example on pgs 170-171 in the book to demonstrate the actual performance implications of misaligned writes using nvprof.

## Slide 53: Global Memory and Special-Purpose Memory
Global memory is widely useful and as easy to use as CPU DRAM
Limitations
  Easy to find applications with memory access patterns that are intrinsically poor for global memory
  Many threads accessing the same memory cell  poor global memory efficiency
  Many threads accessing sparse memory cells  poor global memory efficiency
Special-purpose memory spaces to address these deficiencies in global memory
  Specialized for different types of data, different access patterns
  Give more control over data movement and data placement than CPU architectures do

## Slide 54: Shared Memory
Shared Memory
Transfer
Declared with the __shared__ keyword
Low-latency, high bandwidth
Shared by all threads in a thread block
Explicitly allocated and managed by the programmer, manual L1 cache
Stored on-SM, same physical memory as the GPU L1 cache
On-SM memory is statically partitioned between L1 cache and shared memory

## Slide 55: Shared Memory Allocation
Shared memory can be allocated statically or dynamically
Statically Allocated Shared Memory
  Size is fixed at compile-time
  Can declare many statically allocated shared memory variables
  Can be declared globally or inside a device function
  Can be multi-dimensional arrays
      __shared__ int s_arr[256][256];

## Slide 56: Shared Memory Allocation
Dynamically Allocated Shared Memory
  Size in bytes is set at kernel launch with a third kernel launch configurable
  Can only have one dynamically allocated shared memory array per kernel
  Must be one-dimensional arrays
  __global__ void kernel(...) { extern __shared__ int s_arr[];
  ...
  }
  kernel<<<nblocks, threads_per_block, shared_memory_bytes>>>(...);

## Slide 57: Matvec using shared memory

## Slide 58: Matrix Vector Multiplication

## Slide 59: Matrix Vector Multiplication

## Slide 60: Shared Memory Example: Sum

## Slide 61: Shared Memory as a Managed Cache
1
7
4
13
+
+
+
25
Example: Sum Reduction
Shared memory is explicitly managed and low-latency
  Enables programmer optimizations not possible on CPU architectures
Reduction is a common pattern in computational science that can benefit from manual caching

## Slide 62: Shared Memory as a Managed Cache
1
7
4
13
8
17
Thread 0
Thread 1
25
Step 1
Step 2
Step 3
Implementation 1 of parallel sum reduction
  Note that the global array can be partitioned into subarrays which are themselves independent sequential sum reduction problems

## Slide 63: Shared Memory as a Managed Cache
1
7
4
13
+
+
+
25
1
7
4
13
5
20
Thread 0
Thread 1
25
Step 1
Step 2
Step 3
Thread 0
Thread 1
Implementation 2 of parallel sum reduction
  On the GPU, we change the memory access patterns to improve global memory access coalescing

## Slide 64: Shared Memory as a Managed Cache
__global__ void reduce(int *g_idata, int *g_odata, unsigned int n) {
if (blockIdx.x * blockDim.x + threadIdx.x >= n) return;
int *idata = g_idata + blockIdx.x * blockDim.x; // per-block data
for (int stride = blockDim.x / 2; stride > 0; stride >>= 1) {
// stride accesses from threads in the same thread block
if (tid < stride) idata[tid] += idata[threadIdx.x + stride];
__syncthreads();
}
// output intermediate result from this thread block
if (tid == 0) g_odata[blockIdx.x] = idata[0];
}
global memory access

## Slide 65: Shared Memory as a Managed Cache
__global__ void reduceSmem(int *g_idata, int *g_odata, unsigned int n)
{
__shared__ int smem[DIM];
// set thread ID
unsigned int tid = threadIdx.x;
// boundary check
unsigned int idx = blockIdx.x * blockDim.x + threadIdx.x;
if (idx >= n) return;
// convert global data pointer to local pointer of this block
int *idata = g_idata + blockIdx.x * blockDim.x;
// set to smem by each threads
smem[tid] = idata[tid];
Cache in shared memory

## Slide 66: Shared Memory as a Managed Cache
Shared memory can be used to cache per-block data as a thread block operates on it, rather than going out to global memory every time
Take a look at reduceInteger.cu
  Build and run the code with nvprof
  Which kernels perform best? Which perform worst?
  Use kernel metrics from nvprof to explain performance gains or losses

## Slide 67: Constant Memory
Constant Memory
Constant Cache
Declared with the __constant__ keyword
Read-only
Limited in size: 64KB
Stored in device memory (same physical location as Global Memory)
Cached in a per-SM constant cache
Optimized for all threads in a warp accessing the same memory cell

## Slide 68: Constant Memory
As its name suggests, constant memory is best used for storing constants
  Values which are read-only
  Values that are accessed identically by all threads
For example: suppose all threads are evaluating the equation
                y = mx + b
for different values of x, but identical values of m and b
  All threads would reference m and b with the same memory operation
  This broadcast access pattern is optimal for constant memory

## Slide 69: Constant Memory
A simple 1D stencil
  target cell is updated based on its 8 neighbors, weighted by some constants c0, c1, c2, c3

## Slide 70: Constant Memory
constantStencil.cu contains an example 1D stencil that uses constant memory
  __constant__ float coef[RADIUS + 1];
  cudaMemcpyToSymbol(coef, h_coef, (RADIUS + 1) * sizeof(float));
  __global__ void stencil_1d(float *in, float *out, int N) {
  ...
  for (int i = 1; i <= RADIUS; i++) {
  tmp += coef[i] * (smem[sidx + i] - smem[sidx - i]);
  }
  }
Notes: Instructor note: You can build and run constantStencil.cu to show that it works, but we don’t provide a baseline with global memory with the book so it’s hard to show the improvement. Constant memory performance improvement can be illustrated on the next slides using the wavefront propagation example.

## Slide 71: CUDA Synchronization
When using shared memory, you often must coordinate accesses by multiple threads to the same data
CUDA offers synchronization primitives that allow you to synchronize among threads

## Slide 72: CUDA Synchronization
__syncthreads
  Synchronizes execution across all threads in a thread block
  No thread in a thread block can progress past a __syncthreads before all other threads have reached it
  __syncthreads ensures that all changes to shared and global memory by threads in this block are visible to all other threads in this block
__threadfence_block
  All writes to shared and global memory by the calling thread are visible to all other threads in its block after this fence
  Does not block thread execution

## Slide 73: CUDA Synchronization
__threadfence
  All writes to global memory by the calling thread are visible to all other threads in its grid after this fence
  Does not block thread execution
__threadfence_system
  All writes to global memory, page-locked host memory, and memory of other CUDA devices by the calling thread are visible to all other threads on all CUDA devices and all host threads after this fence
  Does not block thread execution

## Slide 74: Suggested Readings
Chapter 2, 4, 5 in Professional CUDA C Programming
Cliff Woolley. GPU Optimization Fundamentals. 2013. https://www.olcf.ornl.gov/ wp-content/uploads/2013/02/GPU_Opt_Fund-CW1.pdf
Mark Harris. Using Shared Memory in CUDA C/C++. http://devblogs.nvidia.com/ parallelforall/using-shared-memory-cuda-cc/
Mark Harris. Optimizing Parallel Reduction in CUDA. http://developer.download.nvidia .com/assets/cuda/files/reduction.pdf